## Slide 1
DIGITAL TECH
High Performance Computing
MASTER MEIM 2021-2022
Lesson 1
Prof. Livia Marcellino
Prof. of High Performance Computing, Università degli Studi di Napoli Parthenope

## Slide 2: The need for distributed and novel architectures: Moore’s law

## Slide 3
The purpose of a
computer
is to solve problems
super
supercomputing :
solve a problem using a supercomputer

## Slide 4
But…
… is it really necessary to do
high performance computing?
Computers today aim above all
at the speed of applications…
… supercomputers are essential!

## Slide 5
Internet searching…
Million of people query on Google every day

## Slide 6
Weather forecasts
Machine Learning
Financial data mining
whatever the application… it is big data mining

## Slide 7
solve “large scale” (or big data) problems
solve big data problems in "real time” (or useful time)
Supercomputing, in order to

## Slide 8
The time required to run a software depends not only on the number of operations to be done but also on how many operations per second the computer can perform !!!!
How to increase performance?

## Slide 9
a simplified representation of
the software run time required is:
depends on the algorithm
depends on the computer
 = execution time of 1 f.p. operation
T(N) = algorithm
time complexity
= k·T(n) · m
t
k is a multiplicative constant which can depend on practical and stochastic factors:
memory access, CPU occupation for other applications

## Slide 10: How to reduce τ ?
t=k·T(n) · m
.
by reducing T(n)
or
optimizing the algorithm

## Slide 11: To reduce T(n)
It is possible to prove
(complexity theory of algorithms)
that for some classes of problems there are algorithms with minimal computational complexity
(optimal algorithms)
STOP!

## Slide 12
… always to reorganize the algorithm
in order to obtain the most possible algorithm with
minimum time complexity
Numerical
Analysis
However, in general, it is good…
“The fundamental law of computer science: As machines become more powerful, the efficiency of algorithms grows more important, not less.”
[N.Trefethen]
To reduce T(n)

## Slide 13: How to reduce τ ?
reducing 
i.e.
improving technology
(miniaturization process)
= k·T(n) · m
t
m = execution time of 1 f.p. operation

## Slide 14
How did we come to build supercomputers?
almost 80 years ago, in 1945,
the first computer built was a supercomputer!
How to improve the technology?

## Slide 15: Von Neumann machine
In 1945 John Von Neumann introduced an electronic computer scheme, based on the concept of "memorized program":
the instructions are recorded in the "memory" in numerical form.
MEMORY
Output
unit
Input
unit
control
unit
aritmetic
logic
unit
CPU
data & instructions
control
And it is still the basic scheme of current computers

## Slide 16: First type of computer
uses Thermoionic valves
ENIAC (1946)
(Electronic Numerical Integrator And Computer)
It occupied a room of 9x30 square meters
It weighed more than 30 tons

## Slide 17: First generation computer (Thermionic valves: triodes)
First commercial computer
based on thermionics valve technology
UNIVAC-I (1950)
(UNIVersal Automatic Computer I )
It was used in 1952 for the first exit polls of the Americans presidential elections. It correctly anticipated Eisenhower's winnings.
It weighs 5 tons. The central unit is more than 5 meters long and 2.5 meters high.

## Slide 18: Second type of computer
Experimental computer which uses Transistor
TX-0 (1956)
(Transistorized eXperimental computer zero )

## Slide 19: Second generation computer (transistor)
First commercial computer
based on transistor technology.
Siemens 2000 (1957)

## Slide 20: Integrated Circuits - Chip
… idea:
put more transistors on
a plate of germanium
as big as
a postage stamp (1958)
50000 transistor of IBM360 compared to old genration
They can switch in 1/109 seconds

## Slide 21: Third type of computer
First computer with Integrated circuits (Chip)
IBM 360 (1964)

## Slide 22: Third generation computer (chip)
First commercial computer
based on Chip technology.
IBM System/360 (1965-1978)

## Slide 23: integrated circuits (Chip)
more transistors on
a plate of germanium
as big as
a postage stamp (1958)
How many transistors on each chip?

## Slide 24: At this point… … OBSERVATION OF DATA (1965):
COMPONENT COST
COMPONENTS NUMBER PER CHIP
1962
1965
100000$
10000$
1000$
100$
10$
10
100
1000
10000
100000
1
850$
9500$
85
10 transistors on CHIP
85 transistor on CHIP

## Slide 25: Moore’s observation (1965)
“(…) The number of transistors on CHIP has doubled from year to year.(…)”

## Slide 26: MOORE forecast (1965):
COMPONENT COST
COMPONENTS NUMBER PER CHIP
1962
1965
1975
100000$
10000$
1000$
100$
10$
10
102
103
104
1
minimum points
45$
850$
9500$
85
forecast
10 transistor on CHIP
85 transistor on CHIP
65000 transistor on CHIP

## Slide 27: Moore's prediction (1965)
“(…) in 1975 the number of transistors on a chip will be 65,000. (…)”
“The number of transistors will
double every two years.”

## Slide 28: The first microprocessor
Confident in his prediction, in 1968,
Gordon Moore founds Integrated
Electronics Inc (better known as Intel).
In 1971 the Intel created the first microprocessor, made entirely on a single chip.
Among the fathers of the microprocessor there is
the Italian Federico Faggin who is
responsible for its design.
Intel 4004

## Slide 29: Moore's Law
Analyzing the technological evolution of the following years, in 1975 Moore slightly changed his prediction:
“… The computing power of microprocessors will double every 18 months ... "

## Slide 30: Moore's Law
This law has been reflected in practice for over 40 years and has
established a virtuous cycle, pushing technological advances towards better and cheaper products, which in turn push the creation of new applications, which again encourage technological advancement, and so on.
Small Scale Integration
(SSI)
5 transistor
(1964)
Medium Scale Integration
(MSI)
180 transistor
(1968)
Very Large Scale Integration
(VLSI)
132000
transistor
(~1983)
Ultra Large Scale Integration
(ULSI)
7500000
transistor
(1997)
Born of PCs
Large Scale Integration
(LSI)
10000
transistor
(1976)

## Slide 31: However… more transistors
more transistor
decreases μ
Greater heat dispersion
better performance
execution time of 1 f.p. operation
μ

## Slide 32
TECHNOLOGICAL LIMITS
STOP!
To reduce µ: minimize distances
  The miniaturization process cannot proceed indefinitely!
  problems of packaging, cooling and dispersion

## Slide 33: Quantum computers
Despite the advantages obtained, these need important conceptual changes on standard algorithms.
This still represents a limitation today!!!
STOP!
computer with a revised memory (first idea 1980)...
different data storing (different numerical representation), faster access to them.
Quantum algorithms, designed to run on quantum computers.
In February 2019, first commercial quantum computer.

## Slide 34: How to reduce τ ?
t=k·T(n) · m
m = execution time of 1 f.p. operation
B: reducing m
to improve
technology
A: reducing T(n)
to optimize
the algorithm
C: ?
STOP!
STOP!

## Slide 35: C: PARALLEL COMPUTING
Decompose a problem
in more subproblems
and solve them at the same time
with more processing units!
Need to create machines that can distribute the work among them
hardware development

## Slide 36: A survey of HPC architectures: brief history and the Flynn taxonomy

## Slide 37: Temporal parallelism
Many functional units
Temporal parallelism
Pipeline

## Slide 38
parallelism (on-chip)
(multiple functional units within a single ALU)
Output
unit
Input
unit
MEMORY
control
unit
arithmetic
logic unit
Control
data & instructions
CPU
Von Neumann machine

## Slide 39: First type of parallelism
Assembly line technique (pipeline)
TEMPORAL PARALLELISM

## Slide 40: pipelining
Temporal parallelism
Assuming that the different phases of the operation are separable, they are assigned to different functional units, so that when the first unit finishes our work for a phase of operation, it can be dedicated to the next one.

## Slide 41
The use of pipelined functional units is also the basis of:
array processor
capable to operate efficiently
on data structured in array format
Architectures with pipelined functional units

## Slide 42
Architectures with pipelined functional units
The first pipelined system was an IBM System 360/91 (1966):
thanks to the pipeline it obtained an increasing of 33% in performance!
The first microprocessor to use a pipeline:
MOS Technology 6502 (1975)

## Slide 43
Currently
all microprocessors use a pipeline structure to improve their performance.

## Slide 44
Flynn's taxonomy (since 1966)
Computer
SISD
monoprocessor
MISD
pipeline
Michael J. Flynn begins to classify computers...
SISD: Single Instruction - Single Data
MISD: Multiple Instruction - Single Data

## Slide 45: Pipeline: critical issues
The first problem arises from the parallel work of the units:
suppose the pipelined CPU needs to execute the following code
C=A+B
D=C-1
The first statement takes the values stored in variables A and B, then adds them together and finally stores the result in variable C.
The second statement takes the value stored in variable C, subtracts it by one and saves the result in D.
But the second instruction cannot be processed until the data of the first operation is available in memory and then the second operation is stopped and awaits the end of the first one!

## Slide 46: Pipeline: critical issues
The second problem consists in the conditioned jumps.
If the code contains conditional instructions (logical condition) and this condition is not verified, the serial flux of code is interrupted and it shifts towards a new part of the code.
Whenever this happens the microprocessor must perform different operations and then it must empty the pipeline of data in order to upload the new data.
Obviously these operations delay the execution.

## Slide 47: New forms of parallelism:
To overcome the intrinsic limits of temporal parallelism, starting from the 1970s, it was introduced a higher level of parallelism involving several processors
synchronously or asynchronously.

## Slide 48
How the synchronous parallelism
is implemented in a computer?
Parallelism involving several arithmetic-logical units
Second type of parallelism: synchronous
SPATIAL PARALLELISM

## Slide 49
Second type of parallelism
(multiple ALU)
Output
unit
Input
unit
MEMORY
control
unit
arithmetic
logic unit
Control
data & istructions
CPU
Von Neumann machine

## Slide 50: Spatial parallelism synchronous
Several arithmetic-logic units (ALU)
operate following a single control (CU) running in parallel
the same instruction on different data
SIMD computer
(Single Instruction Multiple Data)

## Slide 51
Spatial parallelism synchronous
The Cray-1 (1976) destined to become one of the most famous and most successful supercomputers in history.
A single control unit transmits instructions, which are executed by all processors.
The array processor is especially suitable for computation with matrices and vectors.

## Slide 52
Flynn's taxonomy (since 1966)
Computer
SIMD
SISD
monoprocessor
MISD
Array processors
Connection Machine (1988)
pipeline
Multiple arithmetic-logic units, each with its own operand register, the single flow of instructions acts simultaneously on all units.
In this way, the latency due to the upload of operands is not eliminated, but the number of processed instructions (per second) is increased.
Remember this observation when we will talk about GPUs!

## Slide 53
How the asynchronous parallelism
is implemented in a computer?
Different processors cooperate by executing different instructions on different data
Parallelism involving several CPU=ALU+CU
Third type of parallelism: asynchronous

## Slide 54
Third type of parallelism
(multiple CPU)
Output
unit
Input
unit
MEMORY
Control
unit
arithmetic
logic unit
Control
data & istructions
CPU
Von Neumann machine

## Slide 55: Asynchronous parallelism
More CPUs (ALUs + CUs)
execute in parallel
the different instructions
on different data
Computers MIMD
(Multiple Instruction Multiple Data)

## Slide 56
Flynn's taxonomy (since 1966)
Computer
SIMD
MIMD
SISD
monoprocessor
MISD
Array processors
Connection Machine (1988)
pipeline

## Slide 57: MIMD
Computer MIMD with
Shared Memory
(SM)
CPU
1
CPU
2
CPU
N
MEMORY
Computer MIMD with
Distributed Memory
(DM)

## Slide 58
Flynn's taxonomy (since 1966)
Computer
SIMD
MIMD
DistributedMemory
MassiveParallelProcessors
SISD
monoprocessor
MISD
Array processors
Connection Machine (1988)
used to indicate an architecture with independent ALUs or microprocessors working in parallel (IBM RS/6000 SP, Earth Simulator, Blue Gene, ASCI White, ASCI Red, Roadrunner)
pipeline

## Slide 59
Scalable system up to 512 nodes
Each node is composed of:
4-16 64-bit POWER 3 (RISC) processors
Connection between nodes via high-performance switches (star topology)
IBM RS/6000 SP
Examples of computers MIMD-DM-MPP

## Slide 60: Examples of computers MIMD-DM-MPP
ASCI Red
Intel TeraFLOPS MPP architecture
9632 processors
Grid topology
Overall performance: 2.3 Tflop
Peak Performance: 3.2 Tflop

## Slide 61
To create a distributed memory MIMD machine that has undemanding production costs, clusters are generally used, i.e. sets of autonomous computers connected to each other through the I/O interconnections, and therefore with connectors and cables typical of a standard network.
Each computer has its own separate copy of the operating system, which increases the administration costs,
but this drawback can be easily overcome by using
virtual shared memory machines.
MIMD: distributed memory (DM)

## Slide 62
Flynn's taxonomy (since 1966)
Computer
SIMD
MIMD
DistributedMemory
DistributedSharedMemory
MassiveParallelProcessors
SISD
monoprocessor
MISD
Array processors
Connection Machine (1988)
used to indicate an architecture with independent ALUs or microprocessors working in parallel (IBM RS/6000 SP, Earth Simulator, Blue Gene, ASCI White, ASCI Red, Roadrunner)
pipeline
Used to indicate an architecture with virtual shared memory
(CRAY T3E, Windows HPC server 2008)

## Slide 63
Cray T3E
Exemples of computers MIMD-DM-DSM

## Slide 64: MIMD
Computer MIMD with
shared memory
(SM)
CPU
1
CPU
2
CPU
N
MEMORY
Computer MIMD with
distribuited memory
(DM)

## Slide 65
Flynn's taxonomy (since 1966)
Computer
SIMD
MIMD
DistributedMemory
SharedMemory
SymmetricMultiProcessor
SISD
MISD
Used to indicate a multiprocessor architecture in which there are two or more identical processor connected to a single shared memory. (MULTICORE INTEL)

## Slide 66
Second type of parallelism on-chip design of microprocessors with more CORE (cpu)
on the same chip
First type of parallelism
on-chip
multiple functional units
within a single ALU
pipeline evolution (temporal parallelism)

## Slide 67
Multicore
Output
unit
Input
unit
MEMORY
control
unit
logical
Arithmetic
unit
Control
data & instructions
CPU
CU
ALU
CPU
CU
ALU
CORE
CORE

## Slide 68
on-chip parallelism
first type
on-chip parallelism
second type
ILP
(Instruction Level Parallelism)
+ PIPELINE
TLP
(Thread Level Parallelism)
Goal: Increase performance

## Slide 69
All cores share the memory
To distribute subproblems across threads is more efficient than assigning them to different processes
CORE
1
CORE
2
CORE
N
MEMORY
MIMD:
Shared memory (SM) vs distributed memory (DM)

## Slide 70
Processore Intel Pentium M (single core)
Processore Intel core duo
Multicore: examples

## Slide 71
Does Moore's law still hold true?
It is clear that to ensure that the prediction to still be valid
(and the the systems growth and potential do not stop)
is undoubtedly the parallelism

## Slide 72
Currently
all processors
use different forms of parallelism,
and no system can be defined purely sequential anymore.

## Slide 73: Integrated circuits
Small Scale Integration
5 transistor
(1964)
Medium Scale Integration
180 transistor
(1968)
Large Scale Integration
10000 transistor
(1976)
Very Large Scale Integration
132000 transistor
(~1983)
Ultra Large Scale Integration
7500000 transistor
(1997)
Processore Intel core duo
(2006)
“The Processor is the new Transistor” [Rowen]

## Slide 74: Revisiting of Moore's Law
The number of cores per chip will double every two years
(instead of the clock rate)

## Slide 75: Possible hardware configurations
Small cores have reduced functionality
(E.g .: Single precision arithmetic)
or can be grouped into SIMD units
identical core (Intel Quad-Core)
Core of different size and function
(IBM/Sony/Toshiba Cell)
Small and equal cores
(Sun Niagara)
Many small core but different
(Nvidia GPU)

## Slide 76
Computer
SIMD
MIMD
DistributedMemory
SharedMemory
SymmetricMultiProcessor
SISD
MISD
ASymmetricMultiProcessor
Used to indicate a multiprocessor architecture in which there are two or more identical processor connected to a single shared memory. (MULTICORE INTEL)
Used to indicate several CPU (or processor unit) with different roles (cell IBM, GPU (Graphics Processing Unit), nVidia TESLA)
Flynn's taxonomy (since 1966)

## Slide 77
Exemple of computer MIMD-SM-ASMP
CPU: 8 Zen 2 Cores at 3.5GHz
GPU: 1 RDNA 2 at 10.28 TFLOPs, 36 CUs at 2.23GHz
Sony (PlayStation 5) november 2020
Output
unit
Input
unit
MEMORY
Unità
di
controllo
Unità
logico
aritmetica
control
data & istructions
CORE
CORE
CPU
DUAL CORE
Output
unit
Input
unit
MEMORY
control
data & instructions
CPU
Unità
di
controllo
Unità
logico
aritmetica
ZEN 2
ZEN 2
ZEN 2
ZEN 2
ZEN 2
ZEN 2
ZEN 2
ZEN 2
RDNA 2
CELL
Not all cores have
the same function!

## Slide 78: GPU
RDNA 2: GPU for gaming
These small computing unit are called CUDA cores (Nvidia GeForce) or Stream Processors (AMD Radeon), depending on the production house
QUADRO: GPU for computing
GPUs are essentially the same. What differs is:
the size of memory: game cards have less memory, since games do not require as much memory as modeling programs.
the type of cooling: gaming cards are quieter, while computing cards are noisier.
the drivers: the compute cards aim to create 100% accurate images, performing double precision calculations at full speed, the game cards instead aim to increase the performance, even applying small tricks to reduce the accuracy of the rendering, that you would only notice if you analyzed the image frame by frame and zoomed in very closely.

## Slide 79
The Graphics Processing Units (GPUs) which today have gained so much fam, born (in 2000) to be destined for graphic processing.
Their architecture has evolved very rapidly, and it combines almost all the types of parallelism illustrated.