## Slide 1
Introduction to Automation & Control
MASTER MEIM 2021-2022
A cura del prof. Marco Ariola
Prof. di Automatica all’Università degli Studi di Napoli Parthenope
July 28th, 2022

## Slide 2: Let’s start with a video
WHAT IS AUTOMATION?
Take rational decisions in a complex, evolving and partially unknown world, basing on available information
Automation gives the tools to make something accomplish a task automatically
Three fundamental ingredients:
  Measurement
  Control
  Actuation

## Slide 3: What is control?
Control-system engineers often face this question (or, “What is it that you do, anyway?”) when trying to explain their professional field
Loosely speaking, control is the process of getting “something” to do what you want it to do (or “not do,” as the case may be)
The “something” can be almost anything. Some obvious examples: aircraft, spacecraft, cars, machines, robots, radars, telescopes, etc.
Some less obvious examples: energy systems, the economy, biological systems, the human body…
Control is the process of causing a system variable to conform to some desired value, called a reference value
For instance, for a climate-control system, variable = temperature

## Slide 4: Open-loop vs closed-loop control (1/2)
Fundamentally, there are two types of control loops: open-loop control, and closed-loop control.
In open-loop control, the control action from the controller is independent of the "process output" (or "controlled process variable").
A good example of this is a central heating boiler controlled only by a timer, so that heat is applied for a constant time, regardless of the temperature of the building.
In this case, the control action is switching the boiler off and on. The process output is building temperature.

## Slide 5: Open-loop vs closed-loop control (2/2)
In closed-loop control, the control action from the controller is dependent on the process output.
In the case of the boiler analogy, this would include a temperature sensor to monitor the building temperature, and thereby feed a signal back to the controller to ensure it maintains the building at the temperature set on the thermostat.
A closed-loop controller, therefore, has a feedback loop that ensures the controller exerts a control action to give a process output equal to the "reference input" or "set point". For this reason, closed-loop control is also called feedback control.

## Slide 6: Open-loop control
MATHWORKS VIDEO
Open-loop control is easy and works pretty well but if
the model changes or
an external disturbances occur
then the performance are very poor

## Slide 7: Closed-loop control
MATHWORKS VIDEO
Closed-loop control make it possible to tackle both
model changes and
external disturbances
BUT a more complex architecture is needed

## Slide 8: Components of a Feedback Control System
MATHWORKS VIDEO
Controller
Actuator
Plant
Sensor

## Slide 9: Simulating Disturbance Rejection in Simulink
MATHWORKS VIDEO
Hands-on session: download the software and use Simulink

## Slide 10: Simulating Robustness to System Variations in Simulink
MATHWORKS VIDEO
Hands-on session: download the software and use Simulink

## Slide 11: Some applications of feedback control (1/3)
Ecological Wildlife and forest growth management (reference = population)
Control of plant chemical wastes via monitoring lakes and rivers
Air pollution abatement (reference = chemical concentrations)
Water control and distribution
Flood control via dams and reservoirs (reference=water flow rate)
Medical Medical instrumentation for monitoring and control (reference =dosage)
Artificial limbs (prosthesis; reference = limb position)
Artificial pancreas (reference = glucose level)
Home appliances Home heating, refrigeration, and air conditioning via thermostatic control
Humidity controllers; temperature control of ovens (references = desired temperature, humidity)

## Slide 12: Some applications of feedback control (2/3)
Power/energy Power system control and planning
Feedback instrumentation in oil recovery
Optimal control of windmill blade and solar panel surfaces
Optimal power distribution via power factor control
Power electronics for dc-dc conversion, battery chargers, motor controls (references = power level, optimization criteria)
Transportation Control of roadway vehicle traffic flows using sensors
Automatic speed control devices on automobiles
Propulsion control in rail transit systems
Building elevators and escalators (references = vehicle flow rate, speed, position and speed together)

## Slide 13: Some applications of feedback control (3/3)
Manufacturing Sensor-equipped robots for cutting, drilling die casting, forging,
welding, packaging, and assembling
Chemical process control
Tension control windup processes in textile mills (references = position–speed profiles).
Aerospace and
Military Missile guidance and control
Automatic piloting
Spacecraft control
Tracking systems
Nuclear submarine navigation and control
Firecontrol systems (references = position and attitude).

## Slide 14: Example of a feedback control system
Consider the system designed to maintain the temperature of your house/apartment.
We can draw a block diagram, which identifies the major components of the system, and omits unnecessary details. It also highlights the information/energy flows

## Slide 15: Example of a feedback control system
Central component = process or plant, one of whose variables we want to control
Plant = House
Variable = Temperature

## Slide 16: Example of a feedback control system
Disturbance = some system input that we do not control
Disturbance = Heat loss

## Slide 17: Example of a feedback control system
Actuator = device that influences controlled variable
Actuator = Furnace

## Slide 18: Example of a feedback control system
Reference sensor measures desired system output
Output sensor measures actual system output
Compensator or controller = device that computes the control effort to apply to the actuator, based on sensor readings
Thermostat combines the last three functions.

## Slide 19: A more abstract block diagram

## Slide 20: Exercise
Imagine you want to control the level of a fluid in a tank
The variable you want to control is the level of the fluid
The actuator is the pump which delivers fluid to the tank
Describe a possible open-loop control scheme for this system
Describe a possible closed-loop control scheme for this system

## Slide 21: To sum up
What is the difference between open-loop and closed-loop control?
What is required for open-loop control to work well? What are the problems with it?
Closed-loop control can compensate for model errors and disturbances. Are there any problems with closed-loop control, where open-loop control might be better?

## Slide 22
Thanks for the attention
MASTER MEIM 2021-2022