## Slide 2: Question 4
Question
  The quantisation error is calculated
    as the difference between the signal and the closest level
    as the difference between the signal and the farthest level
    as the absolute value of the sampled signal
.

## Slide 3: Quantization
Quantization is the procedure of constraining something from a continuous set of values (such as the real numbers) to a relatively small discrete set (such as the integers)
Quantization replaces each real number with an approximation from a finite set of discrete values (levels)
  values are represented as fixed-point words or floating-point words
  common word-lengths are 8-bit (256 levels), 16-bit (65,536 levels), 32-bit (4.3 billion levels

## Slide 4: Example of quantization
quantization error

## Slide 5: Coding
Amplitude
levels
time
We start with an uniform quantization

## Slide 6: Coding
With N bits K = 2N quantization levels are obtained
  at each level a code of N bits can be associated
3-bit resolution with eight levels

## Slide 7: Bit rate
Bit rate
  number of bits per second
  product between the sampling frequency and the number of quantization bits

## Slide 8: Non-linear quantization
non-uniform quantization

## Slide 9: Logarithmic quantization
uniform
non-uniform
logarithm

## Slide 10: Example
Uniform quantization

## Slide 11: Example
non-uniform quantization

## Slide 12: Comparison
4 bit linear 3 bit logarithmic

## Slide 13: Comparison
Quality
  the dynamic range of the 8-bit logarithmic quantization corresponds to 13-14 bits linear quantizer
Signal to Noise Rate (SNR)
  a 8-bit logarithmic converter is better than a 8-bit linear at low amplitudes, but worse at high amplitudes

## Slide 14: References
Material
  Slides
  Video Lessons
Books
  Signal Processing Book (Ciaramella)
    free download on the e-learning platform
  Discrete-time signal processing, A. V. Oppenheim, R. W. Schafer, J.R. Buck, Upper Saddle River, N.J., Prentice Hall, 1999, ISBN 0-13-754920-2
  Digital Signal Processing, J. Proakis, D. Manolakis, Prentice Hall, 4 edition, 2006