## Slide 2: Question 6
Question
  In the convolutional theorem
    a convolution in the time domain corresponds to a product in the frequency domain
    a product in the time domain corresponds to a convolution in the frequency domain
    a convolution in the time domain corresponds to a convolution in the frequency domain

## Slide 3: Fourier theorem
Theorem
any continuous periodic signal can be obtained by the superposition of simple sine waves, each with its amplitude and phase, and whose frequencies are harmonics of the fundamental frequency of the signal
Continuous periodic signal with period T0
Fourier series

## Slide 4: Fourier transform
Real environments
  non-periodic signals
Direct Fourier Transform
(Syntesis)
Inverse Fourier Transform
(Analysis)

## Slide 5: Discrete Time Fourier Transform
DTFT
Trasformata di Fourier
a tempo discreto inversa
For a discrete sequence x(n)

## Slide 6: DTFT example
Sequence with two pure tones
with 150 and 440 Hz, respectively.
Sampling frquence of 44100 Hz.
Absolute value of the DTFT
0      0  f  22050

## Slide 7: Convolution theorem
x(n)
F
h(n)
F
Highlighting
  A convolution in the time domain corresponds to a product in the frequency domain
Transform

## Slide 8: Modulation theorem (windowing)
x(n)
F
w(n)
F
Highlighting
  The DTFT of the product of sequence corresopnds to a periodic convolution of the single DTFTs
  e.g., FIR con windowing

## Slide 9: Teorema di Parseval
x(n)
F
Energy
|X(ej )|2 Energy Spectral Density

## Slide 10: References
Material
  Slides
  Video Lessons
Books
  Signal Processing Book (Ciaramella)
    free download on the e-learning platform
  Discrete-time signal processing, A. V. Oppenheim, R. W. Schafer, J.R. Buck, Upper Saddle River, N.J., Prentice Hall, 1999, ISBN 0-13-754920-2
  Digital Signal Processing, J. Proakis, D. Manolakis, Prentice Hall, 4 edition, 2006