## Slide 2: Question 7
Question
  The zeros of the system are
    roots of the numerator polynomial
    roots of the denominator polynomial
    roots of the z Transform
.

## Slide 3: z Transform
For continuous time systems
  The Laplace Transform can be considered a generalization of the Fourier Transform
For Discrete time systems
  The z Transform can be considered a generalization of the Discrete Time Fourier Transform

## Slide 4: z Transform
z Transform
  use a generic complex number
  when a DTFT is obtained
  contains further details on the nature of the signal
The z Transform (bilateral) of a sequence x(n)
right unilateral

## Slide 5: z Transform and DTFT
Setting we obtain
For () the z Transform becomes the DTFT

1
R
I
Unit circle
z =ej
z plane

## Slide 6: Region of Convergence
Given a sequence x(n) the set of z values for which the z Transform converges is named
  Region of Convergence
ROC
Rx-
Rx+

## Slide 7: Region of Convergence
Properties
  The outer boundary is a circle or can be extended to infinity
  The inner border is a circle and can be extended to become the origin
If the ROC
  includes the unit circle, this implies convergence of the z-transform also the Fourier transform converges
  does not include the unit circle the Fourier transform it is not absolutely convergent

## Slide 8: Zeros and poles
An important class is the rational function (polynomials ratio in z)
the zeros of the system are roots of the numerator polynomial
the poles of the system are roots of the denominator polynomial

## Slide 9: Example of ROC
R
I
Unit circle
z plane
zero
pole
1
ROC

## Slide 10: Convergence properties
The ROC must be a connected region
The ROC is a ring or a disc in the z-plane centered at the origin
The Fourier Transform of x(n) converges absolutely if and only if the ROC of the z Transform of x(n) comprises the unit circle
The ROC does not contain any pole and is bounded by poles or zeros or infinite
If x(n) is a sequence of finite duration the ROC is the entire z-plane except for possible z = 0 and z = +
If x (n) is the monolateral right the ROC is the outside of a circle (pole amplitude increased up to (possibly) +)
If x (n) is monolateral left the ROC is the inside of a circle (pole different from zero with lower amplitude up (possibly) to 0)
If x (n) is the two-sided ROC consists of a ring in the z plane limited from the inside and from the outside by a pole and in accordance with the property 3 contains no pole

## Slide 11: References
Material
  Slides
  Video Lessons
Books
  Signal Processing Book (Ciaramella)
    free download on the e-learning platform
  Discrete-time signal processing, A. V. Oppenheim, R. W. Schafer, J.R. Buck, Upper Saddle River, N.J., Prentice Hall, 1999, ISBN 0-13-754920-2
  Digital Signal Processing, J. Proakis, D. Manolakis, Prentice Hall, 4 edition, 2006