## Slide 2: Question 16
A waveform of the sound to be generated is computed by using models
Question
  Karplus-Strong method use
    stable coefficients
    the delay line
    a queue

## Slide 3: Sound Synthesis
A waveform of the sound to be generated is computed by using models
Some approaches
  Additive synthesis
  Physical modelling synthesis

## Slide 4: Additive syntheis
Directly from the Fourier Theorem

## Slide 5: Envelope
t
Amp
Attacco
(Attack)
Decadimento
(decay)
Sostegno
(sustain)
Estinzione
(release)
Notes: Per quanto riguarda l’inviluppo
Si possono individuare quattro transitori
  Attacco (attack) in cui l’ampiezza varia da zero alla massima ampiezza.
  Decadimento (decay) in cui l’ampiezza diminuisce fino ad un certo livello.
  Sostegno (sustain) in cui l’ampiezza rimane pressappoco costante.
  Estinzione (release) in cui l’ampiezza diminuisce fino a zero.
5

## Slide 6: Envelope
Flute
Trumpet
Piano
Violin
Wood blocks
Contrabass
Notes: Presentiamo in questa slide alcuni inviluppi caratteristici di alcuni strumenti musicali:flauto, tromba, pianoforte, violino, blocchi di legno, contrabasso
Notiamo che i suoni percussivi come il pianoforte o i blocchi di legno hanno degli inviluppi con dei transitori molto repentini con l’assenza di una fase di sostegno.
I suoni derivanti da vibrazioni di colonne d’aria (flauto e tromba) o corde (violino e contrabasso) hanno dei transitori meno repentini.
L’attacco della tromba, invece, presenta due massimi caratteristici.
L’inviluppo della chitarra segue in modo più morbido l’inviluppo del pianoforte.
I suoni dei vari strumenti possono essere ascoltati considerando i file 4.2.15 da a ad f
6

## Slide 7: Envelope
Notes: Nella seguente figura viene presentato un tipico segnale musicale e il suo inviluppo.
7

## Slide 8: Spectogram
Notes: Quando si vuole realizzare un’analisi di Fourier di un suono musicale, occorre considerare qual è l’evoluzione dello spettro nel tempo.
In questo caso parliamo di spettrogramma che permette di avere un grafico tridimensionale che rappresenta l’evoulzione nel tempo, nella frequenza e nell’ampiezza del segnale. Esso viene realizzato mediante una variante della trasformata di fourier chiamata short time fourier transform.
8

## Slide 9: Physical modelling synthesis
A mathematical model is used
  equations or algorithms to simulate a physical source of sound
    usually a musical instrument
Methodology
  Karplus-Strong algorithm

## Slide 10: Karplus-Strong algorithm
  Karplus-Strong method
    use the delay line
Comb filter
Difference equation
Transfer fuction

## Slide 11: Chord of an acoustic guitar (A - 440Hz)
Using waveguides

## Slide 12: Chord of an acoustic guitar (A - 440Hz)
Ideal chord with dissipation
Lenght of the delay line considering physical parameters
T – Tension of the chord
M – mass
l – length
Fs – sampling frequency

## Slide 13: References
Material
  Slides
  Video Lessons
Books
  Signal Processing Book (Ciaramella)
    free download on the e-learning platform
  Audio digitale, A. Uncini, McGraw-Hill Education, 2006
  Digital Signal Processing, J. Proakis, D. Manolakis, Prentice Hall, 4 edition, 2006