## Slide 2: Question 26
Multimedia Networking
Question
  Error concealment schemes
    attempt to produce a replacement for a lost packet that is different to the original
    attempt to produce a new packet for replacing the original
    attempt to produce a replacement for a lost packet that is similar to the original

## Slide 3: Introduction
Internet telephony
  commonly called Voice-over-IP (VoIP)
Limitations
  IP provides best-effort service
    delay bound
    percentage of packets lost
Scenario
  sender generates bytes at a rate of 8,000 bytes per second
  every 20 msecs the sender gathers these bytes into a chunk
  a chunk and a special header are encapsulated in a UDP segment, via a call to the socket interface
  the number of bytes in a chunk is 20 msecs
  a UDP segment is sent every 20 msecs
  the receiver can simply play back each chunk as soon as it arrives

## Slide 4: Packet loss
UDP segment
  is encapsulated in an IP datagram
  datagram wanders through the network
  it passes through router buffers
  It is possible that one or more of the buffers in the path from sender to receiver is full
    IP datagram may be discarded
Loss elimination
  sending the packets over TCP
  unacceptable for conversational real-time audio applications such as VoIP
UDP is used by Skype unless a user is behind a NAT or firewall that blocks UDP segments (in which case TCP is used)

## Slide 5: Packet loss
Packet loss ratios
  between 1 and 20 percent can be tolerated
    packet loss concealment
  packet loss exceeds 10 to 20 percent (for example, on a wireless link
    no acceptable audio quality

## Slide 6: End to end delay
End-to-end delay
  accumulation of transmission, processing, and queuing delays
  VoIP
    end-to-end delays smaller than 150 msecs are not perceived by a human listener
    delays between 150 and 400 msecs can be acceptable but are not ideal
    delays exceeding 400 msecs can seriously hinder the interactivity in voice conversations

## Slide 7: Packet jitter
Packet jitter
  varying delays
    the time from when a packet is generated at the source until it is received at the receiver can fluctuate from packet to packet
  e.g., different queues for different rooters

## Slide 8: Removing jitter
Fixed playout delay

## Slide 9: Adaptive Playout Delay
Estimate of the average network delay
Estimate of the average deviation of the network delay
Playout of the packets
costant 4

## Slide 10: Forward Error Correction
FEC - FEC mechanism is to send a lower-resolution audio stream as the
redundant information

## Slide 11: Interleaving
Sending interleaved audio

## Slide 12: Error Concealment
Error concealment schemes
  attempt to produce a replacement for a lost packet that is similar to the original
  the simplest form of receiver-based recovery is packet repetition
  methodology based on compressive sensing

## Slide 13: References
Material
  Slides
  Video Lessons
Books
  Computer Networking: A Top-Down Approach, J. F. Kurose, K. W. Ross, Pearson, 6 edition, 2013